## Slide 1: Automated Extra Pipeline Analysis of Applications mapped to Xilinx UltraScale+ FPGAs

## Slide 2: Automated Extra Pipeline Analysis of Applications mapped to Xilinx UltraScale+ FPGAs
Ilya Ganusov1 Henri Fraisse1 Aaron Ng1
Rafael Trapani Possignolo2 Sabya Das1
1Xilinx Inc. {ilya.ganusov}@xilinx.com
2University of California, Santa Cruz {rpossign}@ucsc.edu

## Slide 3
Agenda
Introduction
Pipeline analysis tool in Vivado
Automatic pipeline insertion
Experimental data
Conclusion

## Slide 4: Introduction

## Slide 5: How does pipelining help?
Pipelining can reduce the length of critical paths
  Improve FMax
  Add extra cycles of latency
  Need to balance pipeline registers to preserve functionality

## Slide 6: Limitations of pipelining
Loops cannot be pipelined
  FMax improvement is limited by the slowest loop
Initial state in the presence of loops need to be adjusted
  In most practical applications this requires minor modifications to the design

## Slide 7: Automatic pipeline analysis in Vivado

## Slide 8: Automatic Pipeline Analysis in Vivado
New automatic pipeline analysis
  Automatically analyses design at any SPR stage
Enables rapid design exploration
  Suggests most efficient places to insert registers in RTL
Backward-compatible
  7-series, UltraScale, UltraScale+
Pipeline analysis
Synthesis
Place
Route
Report timing
Bit-stream

## Slide 9: Automatic Pipeline Analysis in Vivado
The tool interface is a TCL command: report_pipeline_analysis [-cell args] [-clocks args] [-max_added_latency arg] [-report_loops]
Report several key metrics (FMax increase, WNS, register count)
  for each clock domain
  for each added stage of latency
+-----------------+---------------+------------------+------------------+------------------+-----------+----------------+----------------+
| Clock | Added Latency | Ideal Fmax (MHz) | Ideal Delay (ns) | Requirement (ns) | WNS (ns)* | Added Pipe Reg | Total Pipe Reg |
+-----------------+---------------+------------------+------------------+------------------+-----------+----------------+----------------+
| SYS_CLK | 0 | 349.00 | 2.87 | 2.31 | -0.56 | n/a | 0 |
+-----------------+---------------+------------------+------------------+------------------+-----------+----------------+----------------+
| SYS_CLK | 1 | 354.69 | 2.82 | 2.31 | -0.51 | 7693 | 7693 |
+-----------------+---------------+------------------+------------------+------------------+-----------+----------------+----------------+
| SYS_CLK | 2 | 356.97 | 2.80 | 2.31 | -0.49 | 5213 | 12906 |
+-----------------+---------------+------------------+------------------+------------------+-----------+----------------+----------------+
| SYS_CLK | 3 | 364.78 | 2.74 | 2.31 | -0.43 | 3613 | 16519 |
+-----------------+---------------+------------------+------------------+------------------+-----------+----------------+----------------+
| SYS_CLK | 4 | 366.12 | 2.73 | 2.31 | -0.42 | 7348 | 23867 |
+-----------------+---------------+------------------+------------------+------------------+-----------+----------------+----------------+
| SYS_CLK | 5 | 537.24 | 1.86 | 2.31 | 0.45 | 20348 | 44215 |
+-----------------+---------------+------------------+------------------+------------------+-----------+----------------+----------------+

## Slide 10: Automatic pipeline insertion

## Slide 11: Automatic Pipeline Insertion
build graph
find loops
time loops
build a pipeline stage
Insert pipeline registers
Synthesis
Place
Route
Report timing
Bit-stream
Pipeline insertion
Optimize
build a pipeline stage

## Slide 12: Building a pipeline stage
Select all pins
Sort pins by criticality
Add most critical pin to stage
Discard pins in Transitive Fanin
Discard pins in Transitive Fanout
Insert pipeline registers
on all stage pins
#pins > 0
Yes
No

## Slide 13: Building a pipeline stage
Select the most critical legal pin that improve most the slack if pipelined
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 14: Building a pipeline stage
Mark all pins in its Transitive Fan-In
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 15: Building a pipeline stage
Mark all pins in its Transitive Fan-Out
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 16: Building a pipeline stage
Select next un-marked critical pin
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 17: Building a pipeline stage
Mark all pins in its Transitive Fan-In
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 18: Building a pipeline stage
Mark all pins in its Transitive Fan-Out
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 19: Building a pipeline stage
Select next un-marked critical pin
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 20: Building a pipeline stage
Mark all pins in its Transitive Fan-In
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 21: Building a pipeline stage
Select next un-marked critical pin
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 22: Building a pipeline stage
Mark all pins in its Transitive Fan-In
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 23: Building a pipeline stage
Mark all pins in its Transitive Fan-Out
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 24: Building a pipeline stage
Extract the cut
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 25: Building a pipeline stage
Insert pipeline registers
LUT
LUT
LUT
LUT
LUT
LUT
I1
I2
O1
I3
I4
I5
O2
O3
I6

## Slide 26: Experimental results

## Slide 27: Experimental setup
Used Xilinx standard QoR suite
Synthesis
Place
Route
Report timing
Bit-stream
Pipeline insertion
Used post-place pipeline insertion
Metric | Min | Max | Avg
clk domains | 1 | 67 | 3
FMax | 10 MHz | 760 MHz | 300 MHz
LUT | 8200 | 464200 | 129600
FF | 3392 | 586475 | 123163
BRAM | 0 | 1152 | 187
DSP | 0 | 2700 | 195
Total designs | 93 |  | 

## Slide 28: Computing potential FMax gain of pipelining
Considered two loop limits
  Initial: critical loop after default P&R flows
  Tight: critical loop after loop-only P&R flow
Distribution of gain is bimodal
  About half of the designs are loop limited
  About 30% of designs can be improved by more than 50%
Chart: Designs
Initial loop: 18% Gmean FMax
Tight loop: 29% Gmean FMax

## Slide 29: Achieved FMax gain with automatic pipelining
FMax improvement greater than initial loop limit in 50% of cases
FMax improvement close to tight loop limit in most cases
Current limiting factors:
DSP cascades
BRAM cascades
Not using SRL for balancing
Chart: Designs
achieved Fmax after pipelining | 0.10967 | 0.089949 | 0.30797 | 0.046777 | 0.19558 | 0.2605 | 0.069316 | 0.13918 | 0.20289 | 0.55588 | 0.56104 | 0.24366 | 0.64394 | 0.28082 | 0.25465 | 0.34359 | 0.43657 | 0.30045 | 0.48568 | 0.081477 | 0.29117 | 0.37584 | 0.49 | 0.23069 | 0.67964 | 0.3477 | 0.1468 | 0.063937 | 0.28021 | 0.49755 | 0.4557 | 0.45 | 0.613 | 0.688 | 0.74 | 0.35 | 0.1614 | 0.21 | 0.79 | 1.08 | 1.25 | 0.87296 | 1.3199 | 1.68 | 2.45
initial loop limit | 0.017 | 0.0182 | 0.0248 | 0.0292 | 0.0314 | 0.033 | 0.0339 | 0.0399 | 0.0507 | 0.0916 | 0.1069 | 0.1136 | 0.1238 | 0.1269 | 0.1429 | 0.1479 | 0.1614 | 0.1754 | 0.1775 | 0.1789 | 0.1952 | 0.2084 | 0.2115 | 0.2497 | 0.2611 | 0.2872 | 0.3198 | 0.3303 | 0.3384 | 0.3799 | 0.4005 | 0.49 | 0.6359 | 0.688 | 0.7261 | 0.8318 | 0.9103 | 1.0022 | 1.0332 | 1.0911 | 1.4203 | 1.4909 | 1.5483 | 2.5232 | 6.0114
Chart: Designs
achieved Fmax after pipelining | 0.10967 | 0.089949 | 0.30797 | 0.046777 | 0.19558 | 0.2605 | 0.069316 | 0.13918 | 0.20289 | 0.55588 | 0.56104 | 0.24366 | 0.64394 | 0.28082 | 0.25465 | 0.34359 | 0.43657 | 0.30045 | 0.48568 | 0.081477 | 0.29117 | 0.37584 | 0.49 | 0.23069 | 0.67964 | 0.3477 | 0.1468 | 0.063937 | 0.28021 | 0.49755 | 0.4557 | 0.45 | 0.613 | 0.688 | 0.74 | 0.35 | 0.1614 | 0.21 | 0.79 | 1.08 | 1.25 | 0.87296 | 1.3199 | 1.68 | 2.45
tight loop limit | 0.0669 | 0.0332 | 0.3113 | 0.1034 | 0.136 | 0.4004 | 0.0581 | 0.16 | 0.2197 | 0.8681 | 0.6025 | 0.3923 | 0.8347 | 0.804 | 0.2974 | 0.443 | 0.5041 | 0.3642 | 0.4857 | 0.3586 | 0.2334 | 0.4809 | 0.4905 | 0.3471 | 0.6918 | 0.3477 | 0.3198 | 0.9547 | 0.3384 | 0.6608 | 0.6043 | 0.9088 | 0.7864 | 0.688 | 0.8313 | 1.9341 | 1.0801 | 1.9517 | 1.8224 | 1.5265 | 1.4203 | 1.4909 | 2.0465 | 2.5232 | 6.0114

## Slide 30: Register utilization for pipelining
In more than 95% of cases the ratio FF:LUT after pipelining is below 2 which is what offers Xilinx architecture
Architecture ratio
DSP based

## Slide 31: Pipelining data across different architectures
Current Xilinx architectures respond well to highly-pipelined designs
  time-borrowing should favor UltraScale+ over UltraScale
Chart: UltraScale vs V7 architectures
| UltraScale(20nm) | UltraScale+(16nm)
before pipelining | 1.29 | 1.78
after pipelining | 1.537 | 2.121
initial loop limit | 1.51 | 2.08
tight loop limit | 1.717 | 2.34

## Slide 32: Conclusion

## Slide 33: Concluding Remarks
Presented the pipeline analysis tool implemented in Vivado
Implemented and evaluated automatic pipeline insertion
Demonstrated its potential on a representative set of designs
  Results are within 10% of theoretical optimal
Showed that the UltraScale / UltraScale+ architectures handle well highly pipelined designs