## Slide 1: Memory Efficient and High Performance Key-value Store on FPGA Using Cuckoo Hashing
Wei Liang, Wenbo Yin, Ping Kang, Lingli Wang
State Key Laboratory of ASIC and System, Fudan University, China
Notes: HI, My name is liang wei , from Fudan University, China
My topic is memory efficient and high performance key-value store on FPGA using Cuckoo hashing

## Slide 2: Key-value Store
Entry
  Key-value pair
Operations
  Insert ( key, value)
  Search ( key )
  Delete ( key )
Solution
  Hash Table
Notes: Key value store are designed to manage Key value pair. It like the map structure in c plus plus.
We can insert a key value pair, then search or delete with only the key.
The general method to implement key value store is hash table.

## Slide 3: Hash Table
Array T [0,1,…,K-1]
Hash Function: h(x)
Key value pair: {key, value}
T[h(key)] = {key, value}
Hash collision
  h(key1) == h(key2) …
  Linked list
  Cuckoo hashing [Pagh 2004]
Notes: In a hash table, an array with k buckets is used to store KVPs,.
the address of each KVP is calculate by the hash function.
But when multiple keys generate the same hash value, this will cause hash collision.
The solution in software is linked list.
For FPGA implementation, we look at the cuckoo hashing.

## Slide 4: Cuckoo Hashing
Using d hash functions：h1(x), h2(x), …, hd(x)
Each key has d buckets, but it should be stored in one of them
Constant search time
Insert scheme: kick and reinsert process
  Empty bucket valid: select a empty one of d buckets
  No empty bucket: kick a old KVP and take its bucket then reinsert the kicked KVP
Notes: To implement KVS on FPGA, we look at the Cuckoo hashing.
In cuckoo hashing, d hash functions are used for each KVP.
So each KVP has d buckets, but is should be stored in one of them,
This will provide constant search time of fpga implementation, because we can easily compute d hash function concurrently.
However, the insert scheme is complex.
If there is empty one in thess d buckets, we just insert it.
If there is no empty one for the input KVP, we have to select a old KVP and take its bucktes..
Then we have to reinsert the kicked KVP.
This number of this kick and reinsert loop is dependent on the load factor of hash table.

## Slide 5
Direct Storage
  Reduce memory allocated, ;
  size
  : load factor; : the number of KVPs.
More memory efficient when y is much larger than x
Reduce memory bandwidth for kicking and reinserting process
Access value array once for each operation
Decoupled Storage [5]
Notes: The first change is the decouple storage is applied into the Cuckoo hashing;
In the direct Storage, keys and values are stored in the same bucket.
In most applications, the value size is much larger than the key size. So this waste a lot of memory allocated for the value.
Based on this observation, the decoupled storage is applied to Cuckoo hashing for high memory utilization.
In the decoupled storage, keys and value addresses are stored in key arrays
and values are stored in value array. This design can save a lot of memory for the long value application.
Besides, in the decouple storage, only the key and the value address need to be kicked and reinserted. This can reduce memory bandwidth required.
On the other hand, if the value array is implemented using DRAM memory, the decoupled storage only needs to access DRAM memory once for each operation, the latency will be much lower than the simple direct storage.

## Slide 6: Pipeline Scheme
Simple data path: The data path of the insert operation has a feedback path.
  The kicking cycle is not determined. The KVS has to stall during all the kicking cycle
Divided data path of insert: The KVS only need one clock cycle stall for each kicking cycle
Notes: After the decoupled storage, the data path of each operations can be show as this picture It can be divided into three phase, first is hashing , then read key array, the last phase is different in three operations.
The data path of search can be easily mapped to a pipeline structure.
But the path of insert operation has a feedback cycle. And this kicking cycle is undetermined. The KVS has to stall during all the kicking cycle.
We divided the insert path to a simple insert and reinsert
So we take every operation as a simple data path .
And can be mapped into a pipeline structure.

## Slide 7: Architecture
Hash: Jenkins hash function[6] is selected;
Search: read key arrays;
Execute: select a key or kick
Kick Regs: Store kicked KVPs ; Compare
Forward: Read after write data hazards
Notes: The input is the key value pair with the operation code, if there is no key kicked out from the execute module,

## Slide 8: Evaluation
Throughput (insert)
  Load factor < 0.7
    1 request per clock cycle
    200 million requests per second
  Load factor = 0.9
    0.73 request per clock cycle
    146 million requests per second
Latency: 40 ns
Chart: The number of operation per clock cycle
| 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9
Insert | 0.99738 | 0.9938 | 0.9883 | 0.97759 | 0.96098 | 0.93424 | 0.89294 | 0.83494 | 0.73651
Search | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Notes: Here is the evaluation result.
The x-axis is the load factor of the KVS,
The y-axis is the throughput measured by the number of operation per clock cycle.
When the load factor is 0.7, the throughput is one request per clock cycle.
The throughput decreases with the load factor increasing.
When the load factor is 0.9, it can still achieve 0.7 questat per

## Slide 9: Thank you!