## Slide 1
Hardware-Software Codesign of RSA for Optimal Performance vs. Flexibility Trade-off
Malik Umar Sharif, Rabia Shahid, Marcin Rogawski, and Kris Gaj George Mason University USA
Supported in part by NIST/U.S. Department of Commerce
under Grant No. 60NANB15D058

## Slide 2: Primary Designers & Co-Authors
Rabia Shahid
Malik Umar Sharif
Marcin Rogawski
PhD Students
in the Cryptographic Engineering
Research Group (CERG) at GMU
Former PhD Student
Cadence Design Systems
San Jose, CA

## Slide 3: Cryptography at Crossroads
Traditional
Cryptography
Post-Quantum
Cryptography
Transition
Period
RSA
Elliptic Curve Cryptosystems
(existing standards)
Hash-based
Code-based
Lattice-based
Multivariate
(emerging standards)
Attacks using
quantum computers
classical computers
Complete collapse
Trusted resistance
Trusted resistance
Limited trust

## Slide 4: Solutions for the Transition Period
Traditional Scheme
(e.g., RSA)
Post-Quantum Scheme
(e.g., NTRU)
Maximum flexibility with the choice of parameters and key sizes
Hardware acceleration crucial because of high-computational complexity

## Slide 5: Why RSA?
The oldest and most trusted
public key scheme
Baseline for evaluation of
post-quantum cryptosystems
Simple description:
Encryption and decryption
equivalent to modular
exponentiation, Y=XE mod N
Rivest
Shamir
Adleman
MIT, 1977

## Slide 6: Basic Operations of RSA
Mod Exp
Mod Mul
Modular Exponentiation: Y = XE mod N
Modular Multiplication: C = A∙B mod N
Typical operand sizes: 512-2048 bits

## Slide 7: Our Platform – Zynq-7000 & ZedBoard
  Processing System (PS) – ARM based Microprocessor System
Software in C based on RELIC (Efficient LIbrary for Cryptography)
  Free
  Optimized for embedded systems
  Programmable Logic (PL) – a 28nm Artix-7-based reconfigurable logic
Hardware in VHDL based on architecture by Orup-Suzuki
  DSP-unit based
  Optimized for maximum clock frequency

## Slide 8: Design Options
Mod Exp
Mod Mul
Mod Exp
Mod Mul
Mod Exp
Mod Mul
Software in C
Hardware in VHDL
Most Flexible
Least Efficient
Most Efficient
Least Flexible
Best Balanced

## Slide 9: Features of our Solution
Mod Exp
Mod Mul
Three modular exponentiation schemes:
  Left-to-Right (L2R),
  Right-to-Left (R2L)
  Sliding Window (SLID)
selected at run time
Four operand sizes:
  512, 1024, 1536, 2048 bits
selected at run time
Maximum flexibility
and scalability

## Slide 10: Speed-up vs. Software Based on RELIC
Chart: 
| Left-to-Right | Right-to-Left | Sliding Window
512 | 28.51 | 28.42 | 22.47
1024 | 48.48 | 45.47 | 36.33
1536 | 53.62 | 53.6 | 42.91
2048 | 57.67 | 57.65 | 46.25

## Slide 11: Future Work
Implementation of selected post-quantum cryptographic algorithms on Zynq using the similar software/hardware co-design approach
Implementation of the hardware portions using High-Level Synthesis
http://cryptography.gmu.edu
Poster: 3:30-4:15pm