## Slide 1: AdapNoC: A Fast and Flexible FPGA-based NoC Simulator
26th International Conference on Field-Programmable Logic and Applications Lausanne, Switzerland, 29th Aug. – 2nd Sep., 2016
Hadi Mardani Kamali and Shaahin Hessabi
Department of Computer Engineering Sharif University of Technology, IR

## Slide 2: Outline
Motivation
Approach
Proposed Architecture
  Router µArchitecture
  Dual-clock TDMA-based Virtualization
  TGs/TRs migration to system-side
Summary
  Configurable parameters
Evaluation Results
Conclusion
2/31

## Slide 3: Motivation
Increasing the number of cores
  Many-core systems
  Approximately 100 to 1000 cores
Inefficient software simulators
  Low throughput
  Inability to simulate many-core systems
  Difficulties in implementing cycle-accuracy
Inflexible FPGA-based simulators
  Restricted configurable parameters
  Design and run complexity
3/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 4: Motivation (Cont.)
Software-based simulators
  Easy to develop, modify, and run
  Integration capability with full-system simulators
  Too slow in larger networks
  Inability to simulate and assess many-core systems
4/31
BOOKSIM
Cycle-accuracy
Integration with GEM5
SICOSYS
Integration with RSIM
Integration with GEMS
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 5: Motivation (Cont.)
FPGA-based simulators
  High throughput
  Scalability (size has no effect on throughput)
  Ability to implement many-core systems
  Inflexibility
  Design and Simulation Complexity
5/31
FOLCS [2015] | 16×16 Mesh(virt.) | DoR (XY) | Syn. | 5-port , 4-VC 5-stage pipe | RS232 | C on host PC | 17x-22x | - | TDMA based
AdapNoC |  |  |  |  | ?!? |  |  |  | 
NoC Simulators | Topology | Routing | Traffic Pattern | Router µArch. | HW/SW Interface | SW side tool | Speedup (/BOOKSIM) | Re-synth. Solution | Virtualization
Papamichael [2011] | 4×4 Mesh Torus | DoR (XY) | Syn. | 4/8/12/16-port 2/4/8-VC | RS232 | C on host PC | 28x | - | TDMA based
AcENoCs [2011] | 5×5 Mesh | DoR (XY) | Syn. + Trace | 5-port 2-VC 1-stage pipe | RS232 | on-chip soft-core | 14x-47x | - | -
DART [2014] | 7×7 Mesh irregular | DoR (XY) | Syn. + Trace | up to 8-port up to 4-VC 5-stage pipe | PCIe | C on host PC | 100x | Yes | TDMA based
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 6: AdapNoC Approach
Simulating adaptive routing algorithms
  Centralized traffic aggregator
    Gathering traffic information from intermediate queues
    Implementing an adaptive routing algorithm sample
      ATDOR
Dual-clock virtualization methodology
  Minimizing overhead time of unparalleled process
  Implementing a sharable Time Division Multiplexing
TGs/TRs migration to software side
  Maximizing the feasible number of simultaneous nodes on FPGA
  Handling trace-driven (dynamic) traffic
6/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 7: AdapNoC Overall Comparison
FPGA-based simulators
7/31
FOLCS [2015] | 16×16 Mesh(virt.) | DoR (XY) | Syn. | 5-port , 4-VC 5-stage pipe | RS232 | C on host PC | 17x-22x | - | TDMA based
AdapNoC | 32×32 Mesh Torus (virt.) | DoR + Adaptive | Syn. + Trace | 5-port up to 4-VC (3+)-stage pipe | PCIe | on-chip soft-core | 53x-180x | Yes | Dual-clock TDMA based
NoC Simulators | Topology | Routing | Traffic Pattern | Router µArch. | HW/SW Interface | SW side tool | Speedup (/BOOKSIM) | Re-synth. Solution | Virtualization
Papamichael [2011] | 4×4 Mesh Torus | DoR (XY) | Syn. | 4/8/12/16-port 2/4/8-VC | RS232 | C on host PC | 28x | - | TDMA based
AcENoCs [2011] | 5×5 Mesh | DoR (XY) | Syn. + Trace | 5-port 2-VC 1-stage pipe | RS232 | on-chip soft-core | 14x-47x | - | -
DART [2014] | 7×7 Mesh irregular | DoR (XY) | Syn. + Trace | up to 8-port up to 4-VC 5-stage pipe | PCIe | C on host PC | 100x | Yes | TDMA based
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 8: AdapNoC Overall Architecture
Hybrid Architecture
8/31
Hardware (Logic Side)
Interconnection Network Components
Software (System Side)
Dual-Processor Arch.
Router MicroArch.
Crossbar
Routing Algorithm
Flit Queues
MB1
Host + Trace
MB2
Modeling network components
TGs + TRs
Gathering Statistical Information
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 9: Router µ-Architecture
Centralized Vector-based Arch.
  Aggregator
    Monitor routers buffers traffic
    Down-stream flit queues in each port
    Sample scaling
    Aggregate all ports info.
    Send via dedicated port
    Store to traffic load aggregator bank reg.
  Updater
    Pick up all related nodes traffic load info.
    Calculate all source-destination pairs routing
      Consider all congestions
    Renew routing table info
    Send again to routers
9/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 10: Router µ-Architecture
Centralized Vector-based Arch.
  Dedicated vector-based traffic aggregation
    dedicated port aside all N/E/W/S ports
  Source-based routing
  Table-based adaptive routing algorithms
  Complexity of adaptive deadlock-free routing algorithm
    Adaptive Toggle DOR (ATDOR)
      Toggling between XY and YX
      Related to traffic congestion
10/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 11: Router µ-Architecture
Centralized Vector-based Arch.
  Adaptive Toggle DOR (ATDOR) structure
    Source-destination overall toggling
    Consider both XY and YX current congestion info.
    Based on global traffic congestion
11/31
Current_Route == XY
If(Congs. PathXY >= Congs. PathYx) Next_Route = YX
If(Congs. PathXY =< Congs. PathYx) Next_Route = XY
Current_Route == YX
If(Congs. PathXY >= Congs. PathYx)
Next_Route = YX
If(Congs. PathXY =< Congs. PathYx)
Next_Route = XY
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 12: Router µ-Architecture
Centralized Vector-based Arch.
  Traffic load info tables
    Four traffic load tables: E, W, S, N
    scaled number of waiting flits in queues
    Mesh example
12/31
port N |  |  |  |  | 
 | X | 1 | 2 | 3 | 4
Y |  |  |  |  | 
1 |  | 0 | 0 | 0 | 0
2 |  | 2 | 0 | 0 | 0
3 |  | 3 | 0 | 0 | 1
4 |  | 3 | 0 | 0 | 1
port E |  |  |  |  | 
 | X | 1 | 2 | 3 | 4
Y |  |  |  |  | 
1 |  | 0 | 0 | 0 | 0
2 |  | 3 | 3 | 2 | 0
3 |  | 0 | 0 | 0 | 0
4 |  | 0 | 0 | 0 | 0
port S |  |  |  |  | 
 | X | 1 | 2 | 3 | 4
Y |  |  |  |  | 
1 |  | 0 | 0 | 0 | 0
2 |  | 0 | 0 | 1 | 0
3 |  | 0 | 0 | 2 | 0
4 |  | 0 | 0 | 0 | 0
port W |  |  |  |  | 
 | X | 1 | 2 | 3 | 4
Y |  |  |  |  | 
1 |  | 0 | 0 | 0 | 0
2 |  | 0 | 0 | 0 | 0
3 |  | 0 | 0 | 0 | 0
4 |  | 0 | 3 | 3 | 2
For each Node!
Load current routing table
Generate new Toggle Flag (routing table)
Source routing table |  |  |  |  | 
 | X | 1 | 2 | 3 | 4
Y |  |  |  |  | 
1 |  | 1 | 0 | 0 | 0
2 |  | 1 | 0 | 0 | 0
3 |  | 0 | 0 | 0 | *
4 |  | 0 | 0 | 0 | 0
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 13: Router µ-Architecture
Overall router µ-Arch.
  Updatable routing table
  Five-port with (3+) pipeline stage
    Switch setup
    Switch traversal
    Link traversal
  Up to 4 VCs per port
  Credit-based flow control
    Wormhole VC
13/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 14: Dual-clock TDMA-based Virtualization
Virtualization Approach
  Limited FPGA resources
    Restriction in size of simulated network
    P&R complexity and difficulty in implementation phase
    Compulsory reduction in maximum frequency
      Throughput degradation
  Virtualization methodology
    Time Division Multiplexing (TDM) based structure
    Clusters are exclusively implemented on FPGA
      Each cluster has a definite number of nodes
    Serialization simulation
      Each cluster is placed on FPGA in separate time-slots
14/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 15: Dual-clock TDMA-based Virtualization
Cluster-based virtualization
  Up to 16 nodes in each cluster
  Two transmission categories:
    Intra-cluster
      Handled in each time-slot
    Inter-cluster
      Handled non-virtualized buffering BRAM-based queues
15/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 16: Dual-clock TDMA-based Virtualization
Sharing capability of IDLEs in TDM
  Using traffic load tables contents
    Detecting IDLE clusters from down-stream queues
  Sharing time-slots in IDLE clusters
  IDLE cluster
    No intra-cluster transmission
  IDLEness High percentage
    Low injection
    Corner nodes
    Less than 5% channel utilization [Hesse-NoCS-2012]
      In real-world multi-core application
16/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 17: Dual-clock TDMA-based Virtualization
Dual-clock context switching
  Time overhead in TDM
    Wasted clock cycles in context switching
    Especially for high cluster to node ratio sharing time-slots in IDLE clusters
  Dual-clock virtualization structure
    State-handler clock
    System clock
    State-handler freq. / sys. Freq. = 2/1
    Context-switching via state-handler
17/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 18: Dual-clock TDMA-based Virtualization
Dual-clock context switching
  Dual-clock virtualization structure
    State-handler freq. / sys. freq. = 2/1
18/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 19: TGs/TRs Migration to Software Side
Traffic Generators
  Associated with each cluster
  Synthetic
    Random
    Bit-complement
    Transpose
  Dynamic (Trace-driven)
    PARSEC
  Dedicated MB for packet injection + statistics
    Generating synthetic traffic
    Receiving and calculating statistical information
  Dedicated MB for trace-driven traffic
    Receiving and decoding dynamic traffic
19/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 20: TGs/TRs Migration to Software Side
Flit (Source) Queues
  Associated with each port
  FIFO structure as a subset of TG
    Dynamically allocated in run-time
    Equivalent with flit size
Traffic Receptors
  Associated with each cluster
  Decoding received packet information
  Calculating statistical information
    Packet latency
20/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 21: AdapNoC HW Side Summary
A wide range configurable parameters
  Topologies
    Mesh
    Torus
  Routing Algorithms
    Deterministic DOR (XY and YX)
    Adaptive (ATDOR)
  VC/Switch
    Up to 4 VCs per port
    Variable delay link traversal
  Layout
    Virtualized
    Pure
21/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 22: AdapNoC HW Side Summary
A wide range configurable parameters
  (3+)-stage pipelined router µ-architecture
  Number of nodes
    Up to 1024 virtualized
    Up to 64 pure nodes
  Traffic
    Dynamic
      PARSEC
    Synthetic
      Random
      Bit-complement
      Transpose
22/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 23: AdapNoC Overall Comparison
FPGA-based simulators
23/31
FOLCS [2015] | 16×16 Mesh(virt.) | DoR (XY) | Syn. | 5-port , 4-VC 5-stage pipe | RS232 | C on host PC | 17x-22x | - | TDMA based
AdapNoC | 32×32 Mesh Torus (virt.) | DoR + Adaptive | Syn. + Trace | 5-port up to 4-VC (3+)-stage pipe | PCIe | on-chip soft-core | 53x-180x | Yes | Dual-clock TDMA based
NoC Simulators | Topology | Routing | Traffic Pattern | Router µArch. | HW/SW Interface | SW side tool | Speedup (/BOOKSIM) | Re-synth. Solution | Virtualization
Papamichael [2011] | 4×4 Mesh Torus | DoR (XY) | Syn. | 4/8/12/16-port 2/4/8-VC | RS232 | C on host PC | 28x | - | TDMA based
AcENoCs [2011] | 5×5 Mesh | DoR (XY) | Syn. + Trace | 5-port 2-VC 1-stage pipe | RS232 | on-chip soft-core | 14x-47x | - | -
DART [2014] | 7×7 Mesh irregular | DoR (XY) | Syn. + Trace | up to 8-port up to 4-VC 5-stage pipe | PCIe | C on host PC | 100x | Yes | TDMA based
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 24: Evaluation and Results
HW Implementation Consideration
  Verilog HDL
  PLI (DPI)-based debug process
  Microblaze IP-core
  Xilinx Virtex-6 ML605 evaluation board
    XC6VLX240T
  AXI-based interconnection
  PIO-based PCIe interface
    Using DDR3 RAM
24/31
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 25: Evaluation and Results
Average Latency
  4.6% error
    Random attribute
  Packet details
    20K warmup
    45K measurement
25/31
Chart: Injection Rate (flits/node/cycle)
| 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 6.0000000000000005E-2 | 7.0000000000000007E-2 | 0.08 | 0.09 | 9.9999999999999992E-2 | 0.11999999999999998 | 0.13999999999999999 | 0.16 | 0.18000000000000002 | 0.20000000000000004 | 0.22000000000000006 | 0.24000000000000007 | 0.26000000000000006 | 0.28000000000000008 | 0.3000000000000001 | 0.32000000000000012 | 0.34000000000000014 | 0.36000000000000015 | 0.38000000000000017 | 0.40000000000000019 | 0.45000000000000023 | 0.50000000000000022 | 0.55000000000000004 | 0.6
AdapNoC | 16.74 | 16.78 | 16.79 | 16.81 | 16.85 | 16.86 | 16.88 | 16.91 | 16.93 | 16.97 | 17 | 17.09 | 17.14 | 17.19 | 17.25 | 17.32 | 17.4 | 17.55 | 17.74 | 17.98 | 18.23 | 18.44 | 18.72 | 18.98 | 19.38 | 21.75 | 25.31 | 200 | 200
Booksim 2.0 [1] | 15.91 | 15.92 | 15.94 | 15.99 | 16.04 | 16.09 | 16.15 | 16.22 | 16.26 | 16.31 | 16.42 | 16.54 | 16.66 | 16.89 | 17.14 | 17.33 | 17.54 | 17.76 | 17.98 | 18.17 | 18.41 | 18.69 | 19.01 | 19.33 | 19.65 | 21.84 | 25.57 | 200
DART [22] | 18.85 | 18.87 | 18.88 | 18.89 | 18.91 | 18.93 | 18.95 | 18.98 | 19 | 19.03 | 19.11 | 19.17 | 19.24 | 19.31 | 19.37 | 19.43 | 19.48 | 19.56 | 19.64 | 19.71 | 19.79 | 19.88 | 19.97 | 20.06 | 20.17 | 22.16 | 25.91 | 200 | 200
Parameters
Topology
Link Latency
Routing Algorithm
Traffic Pattern
Number of VCs
Input VC buffer size
Packet Size
Case 1
3×3 mesh
1 cycle
XY
random
2
4
2
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 26: Evaluation and Results
Adaptive evaluation
26/31
Parameters
Topology
Link Latency
Routing Algorithm
Traffic Pattern
Number of VCs
Input VC buffer size
Packet Size
Case 2
8×8 mesh
1 cycle
ATDOR
random
2
4
16
Chart: Injection Rate (flits/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48 | 0.5 | 0.52 | 0.54 | 0.56000000000000005 | 0.57999999999999996 | 0.6 | 0.62 | 0.64
AdapNoC deterministic XY | 52.4353 | 52.4626 | 52.4789 | 52.5721 | 52.5939 | 52.6366 | 52.6792 | 52.7219 | 52.7645 | 52.8195 | 52.8544 | 52.8981 | 52.9415 | 52.9848 | 53.024 | 53.0674 | 53.1095 | 55.1562 | 58.8517 | 63.4086 | 73.0125 | 97.1517 | 200
AdapNoC adaptive XY | 50.3662 | 50.3812 | 50.4105 | 50.4312 | 50.451 | 50.4744 | 50.4917 | 50.5177 | 50.539 | 50.5634 | 50.5871 | 50.611 | 50.6343 | 50.6581 | 50.6817 | 50.701 | 50.7286 | 50.7545 | 50.7764 | 50.7912 | 50.8236 | 50.8451 | 52.1254 | 54.9812 | 59.0127 | 67.0395 | 78.9128 | 101.1254 | 200
Centralized ATDOR [29] | 49.9851 | 50.0115 | 50.0431 | 50.0805 | 50.117 | 50.1473 | 50.1806 | 50.2138 | 50.2471 | 50.2804 | 50.3137 | 50.347 | 50.3802 | 50.4135 | 50.4468 | 50.4801 | 50.5134 | 50.5466 | 50.5799 | 50.6132 | 50.6465 | 50.6798 | 50.713 | 50.7463 | 52.1254 | 54.9812 | 59.0127 | 67.0395 | 78.9128 | 101.1254 | 200 | 200
O1Turn [33] | 48.9571 | 48.9832 | 49.033 | 49.0804 | 49.0935 | 49.1424 | 49.1782 | 49.2151 | 49.2523 | 49.2896 | 49.3264 | 49.3636 | 49.4111 | 49.4381 | 49.4753 | 49.5124 | 49.5482 | 49.5863 | 49.6238 | 49.661 | 49.6981 | 49.7352 | 49.7726 | 49.8095 | 51.1285 | 53.5456 | 57.151 | 64.1895 | 75.124 | 95.1245 | 119.14 | 200
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 27: Evaluation and Results
Resource Utilization
  8×8 mesh
  non-virtualized
  Just 72% Res. Util.
27/31
5564 | 2472 | 13%
11456 | 4856 | 18%
4391 | 3857 | 9.5%
3265 | 1650 | 7.5%
2126 | 205 | 2%
1154 | 165 | 1%
Parameters
Flit Queue
Router
Crossbar Switch + Arbiter
Traffic Aggregator and Updater
PCIe and AXI4 Core
MICROBLAZE controller
Slices | Registers | % of Utilization
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 28: Evaluation and Results
Different network size
  Mesh
    2×2
    3×3
    4×4
    5×5
    6×6
    7×7
    8×8
  Virtualization impact!
28/31
Chart: Injection Rate
| 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6
2×2 | 699732 | 608162 | 491022 | 441982 | 399012 | 355102 | 320123 | 305401 | 292100 | 270100 | 263192 | 251092
3×3 | 401924 | 346150 | 304967 | 285010 | 268000 | 249810 | 239010 | 221975 | 204575 | 195690 | 182980 | 171651
4×4 | 330102 | 301900 | 275641 | 251091 | 226891 | 203097 | 182920 | 168258 | 154230 | 145689 | 136711 | 130976
5×5 | 281092 | 257861 | 228615 | 205145 | 182765 | 163875 | 145871 | 131090 | 118672 | 99865 | 95884 | 88791
6×6 | 251690 | 226710 | 206757 | 181854 | 162712 | 141659 | 127670 | 111092 | 92874 | 84765 | 77901 | 74912
7×7 | 222954 | 199201 | 180231 | 162765 | 138975 | 122910 | 104561 | 85541 | 71480 | 62760 | 60120 | 56182
8×8 | 199201 | 180201 | 155621 | 144001 | 121029 | 106724 | 81845 | 64455 | 50301 | 40912 | 36120 | 31924
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 29: Evaluation and Results
Virtualization
  Sharable time-slot
  Dual-clock architecture
    Context-switching
29/31
Chart: Injection Rate (flits/node/cycle)
| 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45
AdapNoC | 3.45 | 6.07 | 7.89 | 9.61 | 11.19 | 12.34 | 13.23 | 14.17 | 14.67
DART [22] | 7.11 | 8.61 | 9.69 | 10.91 | 11.88 | 12.78 | 13.62 | 14.44 | 14.87
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 30: Evaluation and Results
Simulation speed
  Comparison with baselines
    DART
    AcENoCs
30/31
Chart: Injection Rate
| 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5
AdapNoC | 276521 | 251261 | 221256 | 197514 | 177004 | 155732 | 138722 | 126622 | 111057 | 95125
AcENoCs [20] | 73120 | 58129 | 48124 | 41191 | 34650 | 28193 | 25671 | 25617 | 25155 | 24918
DART [22] | 146240 | 142141 | 136125 | 131029 | 126512 | 121251 | 117125 | 112125 | 104125 | 99672
Motivation
Approach
Router µArch.
Dual-clock
TGs/TRs Migr.
Summary
Eval. Result

## Slide 31: Summary
Software-configurable FPGA-based NoC simulator
  Adaptive routing algorithms simulation
    Centralized traffic aggregator
      Gathering traffic information from intermediate queues
      Implementing an adaptive routing algorithm sample
        ATDOR
  Dual-clock virtualization methodology
    Minimizing overhead time of unparalleled process
    Implementing a sharable Time Division Multiplexing
  TGs/TRs migration to software side
    Maximizing the feasible number of simultaneous nodes on FPGA
    Handling trace-driven (dynamic) traffic
31/31