## Slide 1: The Speed of Diversity: Exploring Complex Interconnect Topologies for the Global Metal Layer
Oleg Petelin and Vaughn Betz
FPL 2016

## Slide 2: Motivation – The Metal Stack
Poor wire RC scaling  more complex metal stack
Lower layers:
  Many wires, high RC delay
Upper layers:
  Few wires, low RC delay
Connecting to upper layers:
  Deep via stack
Intel 14nm Metal Stack
Introduction

## Slide 3: Motivation – The Metal Stack
Metal Layer | Pitch | RC Speedup
Intermediate | 48 nm | 1x
Semi-Global | 96 nm | 7x
Global | 192 nm | 50x
22nm, ITRS 2011 Interconnect Report
Introduction
Per-tile Delay (ps)
80
70
60
50
40
30
20
10
0
Global metal layer: small gain for short wires
But essential for useful longer wires

## Slide 4: Contributions
FPGA routing architecture to exploit metal stack
  Scarce but faster global wires
  Plentiful but resistive semi-global wires
  Simultaneously explore:
    Segment lengths
    Layer used for each wire type
    Switch patterns and interconnect hierarchies
Requires CAD Enhancements
  New VPR switch block language  arbitrary switch patterns
  VPR router enhancements  optimize for arbitrary interconnect
Introduction

## Slide 5
CAD Enhancements

## Slide 6: Enhanced Switch Block Descriptions
CAD Enhancements
<switchblock>
…
…
Concise, human-readable, general
description format
…
…
</switchblock>
Architecture Description File:
Multi-Gigabyte Routing Resource Graph
Want to turn this…
… into this

## Slide 7: Enhanced Switch Block Descriptions
Current – limited flexibility:
  Specify which tracks connect
  Regardless of wire type and whether wire end or midpoint
VPR 7.0 patterns hard-coded:
  Switch pattern in one keyword, e.g. Wilton, Universal, …
New – more flexible & general
  Distinguishes between wire types and wire endpoints/midpoints
  Uses mathematical permutation functions (not keywords) to implement connections
0
1
0
1
1
0
0
1
0
1
2
3
0
1
3
2
CAD Enhancements
Left  Right
L2 endpoints  L2 endpoints
Permutation = t+1
Left  Top
L2 midpoints L3 endpoints
Permutation = t
Right  Bottom
L3 mid/endpoints  all endpoints
Permutation = W-t
L3
L2

## Slide 8: Enhanced Router Lookahead
How to route a connection?
BFS  Simple, impractically slow
Fast routers use a lookahead to estimate remaining cost from intermediate routing points
Good lookahead  fast, directed routing
CAD Enhancements

## Slide 9: Enhanced Router Lookahead
How to estimate remaining cost?
  VPR 7.0: assume the same wire type can be used to finish the route in an optimal number of segments
   Efficient, limiting
  Independence: makes absolutely no assumptions about the FPGA architecture to build large lookup tables of routing costs
   Very general, very memory-hungry
  (multiple GBs for 200 x 200 FPGA)
  Proposed: perform BFS sample routings to build lookup tables of routing costs for each relative coordinate offset
    Exploit symmetries that exist in island-style FPGAs
     Fast, memory efficient, handles complex interconnect
    (10s of MBs for 200 x 200 FPGA)
CAD Enhancements
Lookup[wire type A][x-chan][1][3] = 0.6ns
Lookup[wire type B][y-chan][5][5] = 1.3ns
From wire type
From channel
|Δx|
|Δy|
Notes: - Add slide 6

## Slide 10: Enhanced Router Lookahead
CAD Enhancements

## Slide 11
Complex Interconnect Exploration

## Slide 12: Exploration Methodology
22nm architectures generated with COFFE
85% semi-global layer wires
15% global-layer wires
Deep via stack layout difficulties  Global wires have connections every 4 tiles
Complex Interconnect
Unidirectional Switches
semi-global
global
L=4
L=8

## Slide 13: Exploration Methodology
Benchmark | #6-LUTs
mcml | 99,700
LU32PEEng | 75,530
bgm | 30,089
stereovision2 | 29,849
LU8PEEng | 21,954
stereovision0 | 11,462
stereovision1 | 10,366
blob_merge | 6,016
mkDelayWorker32B | 5,580
Complex Interconnect
Parameter | Primary Arch | Arch for Verification
Logic Block | Ten 6-LUTs | Eight 4-LUTs
Logic Block Crossbars | Input | None
Block RAM | 32K | 18K
DSP | 36x36 | 36x36
Channel Width | 300 | 200
Connection Block Flex | 0.1 | 0.2
Semi-Global Wirelength | 4 | 2
Global Wirelength | 4, 8, 16 | 4, 8, 16
Interconnect Hierarchy | Discussed Later | Discussed Later
Architecture:
9 Largest VTR Benchmarks:

## Slide 14: Complex Topologies Explored
85%, L4
15%, global
(1) On-CB, Off-CB
85%, L4
15%, global
(2) On-CB, Off-SB
85%, L4
15%, global
(3) On-CB, Off-CB/SB
55%, L4
15%, global
30%, L4*
(4) On-SB, Off-SB
75%, L4
15%, global
10%, L4*
(5) On-CB/SB, Off-CB/SB
Complex Interconnect
Topology name represents connectivity of wires on global metal layer
  CB: Connection Block
  SB: Switch Block

## Slide 15: Routing Example – “On-CB, Off-CB”
85%, L4
15%, global

## Slide 16: Routing Example – “On-SB, Off-SB”
55%, L4
15%, global
30%, L4*

## Slide 17: VPR 7.0 Default
Connects to wire segment start points without distinguishing between wire types
Connects tracks using Wilton permutation function, with unidirectional legalization
Chart: Global Wire Segment Length
| 4 | 8 | 16
VPR 7.0 Default | 8.03 | 8.6 | 9.35
Complex Interconnect
85%, L4
15%, global
Only semi-global layer wires
Notes: Add no global wire point.

## Slide 18: (1) On-CB, Off-CB
Regular and fast wires form distinct routing networks
  Used in previous published studies
Worse delay than VPR default (Wilton over all wires)
Deep via stack restrictions  global wires too hard to use
Chart: Global Wire Segment Length
| 4 | 8 | 16
VPR 7.0 Default | 8.03 | 8.6 | 9.35
On-CB, Off-CB | 8.73 | 9.12 | 9.51
85%, L4
15%, global
Complex Interconnect

## Slide 19: (2) On-CB, Off-SB
On-CB  every output pin is guaranteed a connection to fast routing
Off-SB  increased routing flexibility compensates for decreased flexibility from deep via stacks
Routing delay improved by 5-11%
Chart: Global Wire Segment Length
| 4 | 8 | 16
VPR 7.0 Default | 8.03 | 8.6 | 9.35
On-CB, Off-CB | 8.73 | 9.12 | 9.51
On-CB, Off-SB | 7.75 | 7.93 | 8.31
85%, L4
15%, global
Complex Interconnect

## Slide 20: (3) On-CB, Off-CB/SB
Global wires driving switch blocks AND connection blocks adds a small amount of extra routing flexibility
More switches, but not much gain
Chart: Global Wire Segment Length
| 4 | 8 | 16
VPR 7.0 Default | 8.03 | 8.6 | 9.35
On-CB, Off-CB | 8.73 | 9.12 | 9.51
On-CB, Off-SB | 7.75 | 7.93 | 8.31
On-CB, Off-CB/SB | 7.62 | 7.74 | 8.42
85%, L4
15%, global
Complex Interconnect

## Slide 21: (4) On-SB, Off-SB
Connect to global-layer wires exclusively through regular routing wires
Improves the delay of long wire segments
  Driving long global wires from regular routing adds much-needed flexibility
Long global-layer wire delay improved by 14%
Chart: Global Wire Segment Length
| 4 | 8 | 16
VPR 7.0 Default | 8.03 | 8.6 | 9.35
On-CB, Off-CB | 8.73 | 9.12 | 9.51
On-CB, Off-SB | 7.75 | 7.93 | 8.31
On-CB, Off-CB/SB | 7.62 | 7.74 | 8.42
On-SB, Off-SB | 8.14 | 7.97 | 8.08
Complex Interconnect
85%, L4
15%, global
14%
delay
red.

## Slide 22: (5) On-CB/SB, Off-CB/SB
Little improvement over previous topologies for all global wire segments lengths
Connection blocks add little routing flexibility to fast wiring given deep via stack restrictions
Chart: Global Wire Segment Length
| 4 | 8 | 16
VPR 7.0 Default | 8.03 | 8.6 | 9.35
On-CB, Off-CB | 8.73 | 9.12 | 9.51
On-CB, Off-SB | 7.75 | 7.93 | 8.31
On-CB, Off-CB/SB | 7.62 | 7.74 | 8.42
On-SB, Off-SB | 8.14 | 7.97 | 8.08
On-CB/SB, Off-CB/SB | 7.61 | 7.81 | 8.06
Complex Interconnect
85%, L4
15%, global

## Slide 23: Verifying Results with Different Logic Block Architecture
4-LUT logic block without input/output crossbars
Trends similar to 6-LUT arch
But lack of internal crossbars makes switch block connections between semi-global and global wires more important
Complex Interconnect
Chart: GLOBAL WIRE SEGMENT LENGTH
| 4 | 8 | 16
VPR 7.0 Default | 6.99 | 6.58 | 7.02
On-CB, Off-CB | 8.89 | 9.34 | 9.39
On-CB, Off-SB | 6.05 | 6.77 | 7.94
On-CB, Off-CB/SB | 6.29 | 6.74 | 8.51
On-SB, Off-SB | 6.22 | 6.18 | 6.11
On-CB/SB, Off-CB/SB | 6.23 | 6.25 | 6.38
13%
delay
red.

## Slide 24: Complex Interconnect Summary
Short Global Layer Wires (L=4):
  Drive from connection block  immediate access to fast routing
  Drive regular (semi-global) wires  routing flexibility compensates for deep via stacks
Long Global Layer Wires (L=16):
  Drive from regular (semi-global) wires compensate for few start points of long unidirectional wires
  Drive regular (semi-global) wires
Shorter global-layer wires (L = 4) perform surprisingly well
  Shorter wires have better routing flexibility  more signals can use fast routing
Good “routing hierarchies” reduce delay by 5-14% vs. VPR default switch and 13% - 15% vs. disjoint global / semi-global networks
Complex Interconnect
semi-global
global
semi-global
global

## Slide 25: Summary of Contributions
General but concise switch block description in VPR
  And automatic creation of matching routing resource graph
General but computationally efficient router lookahead
  ~10% faster circuits with complex switch patterns
Exploration of interconnect hierarchies to take advantage of routing on the global metal layer
  Good interconnect hierarchy 5-14% faster than VPR’s best prior switch pattern
Conclusions

## Slide 26: Future Work
Deep via stack layout difficulty  restricted global-layer wire connections to one in four tiles
  Repeat explorations when global-layer via connections are allowed every 2, 8, etc. tiles
Considered one global-layer wire type (length) at a time
  Mixes of wire lengths on the global layer may yield further gains
Many new switch fabrics now possible
  Different patterns, unbalanced multiplexer size/flexibility, …
Conclusions

## Slide 27: Thank You! Oleg Petelin opetelin@eecg.toronto.edu Vaughn Betz vaughn@eecg.toronto.edu

## Slide 28: Appendix A
Chart: GLOBAL WIRE SEGMENT LENGTH
| 4 | 8 | 16
VPR 7.0 Default | 15376.0862 | 15167.6333 | 14971.6157
On-CB, Off-CB | 15488.937 | 15248.5457 | 15013.9933
On-CB, Off-SB | 15602.8301 | 15362.2599 | 15127.1852
On-CB, Off-CB/SB | 15658.7644 | 15418.3833 | 15183.8077
On-SB, Off-SB | 15901.0731 | 15582.722 | 15459.8818
On-CB/SB, Off-CB/SB | 15889.6477 | 15575.7384 | 15361.6469
Complex interconnect topology per-tile areas
  6-LUT logic block