## Slide 1: Fast and Robust Hashing for Database Operators
Kaan Kara, Gustavo Alonso
Notes: Welcome everyone. Our research is about accelerating database operators using FPGAs. Since hashing is an essential part of many operators, in this work we focus on how we can do fast and robust hashing using an FPGA as part of a heterogeneous architecture.

## Slide 2: Motivation
Hash tables and hashing very often used in:
Choice of hash function impacts performance:
  Speed: Easily computable Higher hashing throughput
  hash functions
  Robustness: Balanced distribution of Less collisions,
  hash values O(1) look-up, insertion deletion
Query Processing
In Databases
Key-Value Stores
Load Distributing
Middleware
X
Trade-off
Notes: Our motivation comes from a recent work from the database community, which showed the importance of choosing a right hash function depending on the application.
Obviously, hash tables and hashing are often used in applications such as query processing, key-value stores or load distribution.
The choice of the hash function affects performance because of two properties: The first one is how fast the hash function is calculated. Easily computable hash functions lead to a higher hashing throughput. The second one is the robustness. More robust hash functions produce a balanced distribution of hash values, causing less collisions and guaranteeing O(1) look-up, insertion and deletion performance. Unfortunately, there is a trade-off between the speed and the robustness of a hash function. In other words, more robust hash functions are complex and take a longer time to calculate.

## Slide 3: Trade-Off: Fast vs. Robust Hashing
Key distributions:
Linear | Random | Grid | Reverse Grid
0x0000_0001 0x0000_0002 0x0000_0003 … 0x0001_1AF0 … | 0x2E4F_5929 0x82FA_C&B1 0x186C_BA1F … … … | 0x1111_1111 0x1111_1112 0x1111_1113 … 0x111E_14E1 … | 0x1111_1111 0x2111_1111 0x3111_1111 … 0x1E41_E111 …
Chart: Hashing Throughput
| Modulo | Multiply-Shift | Murmur | Simple Tabulation | LookUp3 | City
Hashing Throughput | 1933.5 | 415.7 | 226.7 | 58.4 | 118.2 | 118.4
Chart: Insertions via Linear Probing
| Modulo | Multiply-Shift | Murmur | Simple Tabulation | LookUp3 | City
Linear | 1 | 1 | 2.1735 | 2.1584 | 2.1678 | 2.1634
Random | 2.1686 | 2.1616 | 2.1742 | 2.1602 | 2.1599 | 2.1694
Grid | 0 | 1.6417 | 2.1677 | 2.2045 | 2.1713 | 2.1661
Reverse Grid | 0 | 17.0139 | 2.1683 | 2.1369 | 2.1667 | 2.1659
300k
700k
Inserting 1.5 Million keys into an empty hash table until it is 70% full.
Notes: We performed a set of micro-benchmarks to show this trade-off. For that, we use 4 different key distributions, each representing specific data types. Linear keys represent indexes, then we have randomly distributed keys. The third and fourth distributions we call grid and reverse grid distributions, which resemble strings or address patterns.
First micro-benchmark I will show you is the raw hashing throughput for different hash functions. The bars indicate how fast it is to compute a hash function. For example, modulo being a very simple arithmetic operation achieves the highest throughput.
The second micro-benchmark shows the number of average probes needed, when inserting a value into a hash table. The bars basically indicate here how many hash value collisions occur during this process. We see that modulo and multiply-shift, being non-robust hash functions, produce many colliding values depending on the key distribution. On the other hand, the other hash functions behave in a robust way, not getting affected by the key distribution. This shows the importance of the robustness property.
This is the speed and robustness trade-off. In this work, we try to break it by implementing robust hash functions on an FPGA as part of a heterogeneous platform.

## Slide 4: Target Platform: Intel Xeon+FPGA
Accelerator Function Unit
Written in an HDL
Able to access entire main memory
QPI provides cache-coherency
Acknowledgement: We thank Intel for their generous donation of Xeon+FPGA.
Notes: Our target platform is the Intel Xeon+FPGA, which is a 2 socket machine. On the one socket there is a Xeon CPU with 96 GBs of main memory. On the other one there is a Stratix 5 FPGA. We can implement our accelerators in so called accelerator function units, implemented in an HDL. The accelerators are able to access the entire main memory in a cache-coherent way via the QPI. The QPI provides 6.5 GB/s bandwidth for combined read and writes.

## Slide 5: Hardware Hashing
RTL:
Performance:
Simple Tabulation
Murmur
Chart: Hashing Throughput
| Modulo | Multiply-Shift | Murmur | Simple Tabulation | LookUp3 | City | FPGA (6.5 GB/s) | FPGA (25.6 GB/s)
Hashing Throughput | 1933.5 | 415.7 | 226.7 | 58.4 | 118.2 | 118.4 | 386.9 | 1600
CPU Hashing
FPGA Hashing
Notes: We implemented simple tabulation and murmur hashing on the FPGA. I will not go into implementation details, which you can read in the paper. I would like to focus more on the performance delivered by the FPGA. In this figure we have again the raw hashing throughput, this time with the FPGA results. The measured throughput for FPGA hashing on the target platform reaches multiply-shift on the CPU. But bear in mind that the current implementation is completely memory bound, that is 6.5 GB/s. Actually, the implementation currently clocked at 200 MHz is capable of delivering 1600 Million keys per second. If the bandwidth would be 25.6 GB/s for combined read and write channels, this would be the throughput that we would measure.

## Slide 6: Hybrid Hash Table
1.5 Million keys with 70% fill rate of the hash table
CPU Hashing
Chart: Average Hash Table Build Times
| Modulo | Multiply-Shift | Murmur | Simple Tabulation | LookUp3 | City | FPGA (6.5 GB/s)
Average Hash Table Build Times (ms) | 0 | 30.93 | 31.79 | 60.83 | 40.55 | 40.55 | 24.23
410 s
21%
Notes: In a second step, we integrated the FPGA hashing into a hybrid hash table. We do this, because we would like to show that our FPGA hashing can be integrated into complete applications, as we plan to use this during query processing in the future. When a value needs to be inserted, updated, read or deleted, its key is first hashed on the FPGA and then the hash value is used in software for performing the look-up. This kind of hybrid processing is made possible through the shared memory architecture on the Xeon+FPGA. No batching or extra data copying has to be performed, making acceleration without further overhead possible.
In this figure we present the hash table build times, averaged over the 4 key distributions we presented. The combination of both robustness and high throughput of the FPGA hashing enables us to get the best result, an improvement of 21% compared to the best CPU hashing.

## Slide 7: Thank you for your attention! Visit our poster tomorrow for questions.

## Slide 8: Contact information and credits
ETH Zurich
Systems Group
Universitatsstrasse 6
8092 Zurich
systems.ethz.ch
© ETH Zurich, August 2016